## Slide 1
Data science to support the development of a SSP
- ComplexWorld 2016 Event -
Pablo Hernández-Coronado Quintero
AESA, Spanish Safety and Security Aviation Agency
Data Science in Aviation Workshop
AESA-RAC project
D. Ríos, J. Gómez, C. Alfaro, J. Girón, RAC
V. Elvira, F. Bernal, P. Hernández-Coronado, AESA

## Slide 2
CONTENTS
  State Safety Programme
  RIMAS: Risk Management in Aviation Safety
  Discussion

## Slide 3
SAFETY
  Safety Critical in Civil Aviation
    Increasing complexity of global air transportation system;
    Interrelated and complex nature of aviation activities;
    Traffic growth and;
    Increasing competition forcing cost reduction (even more under crisis)…
    However… relatively simple methodologies and tools for safety risk analysis for commercial aviation operations, mostly based on risk matrices
Need to assure safe operation of aircraft through methodologies and tools supporting evolution of a proactive strategy to improve safety performance
Notes: It is somewhat shocking that while aviation remains one of the most advanced means of transportation, technology wise, the industry and regulators have never implemented any type of modern decision analysis methodologies in this area.
The Spanish Aviation Safety and Security Agency (AESA) developed a scientific-based framework called RIMAS to support safety risk management decisions at State level, taking advantage of safety data infrastructures available.

## Slide 4: STATE SAFETY PROGRAMME?
OUTLINE
Programs
Safety Action Plan
Safety Oversight Plan
Regulations
Safety Campaigns...
policy
Cost/
benefit
evaluation
analysis
rules
Input
Data
Operational
Financial
HHRR
Legal...
Output
Execution programs
SRM
SA

## Slide 5
Sector
Corporate
Safety Cloud
SAFETY CLOUD AND SAFETY RISK ANALYSIS
System

## Slide 6
SAFETY RISK AREAS
SAFETY RISK AREAS/ISSUES
MOR. 90 types of occurrences. Registered in ECCAIRS.
Other databases: ASN, Eurocontrol (CFMU), ESTOP,…
5 severity degrees (ICAO and EUROCONTROL): Minor, Significant, Major, Serious, Accident
4 types of aircrafts T1, T2, T3, T4 (No. of passengers)
Flight operations
  Hard landing,…
Navigation services
  ACAS warnings,…
Airworthiness
  Engine failure,…
Airport
  Impact with vehicle,…
External factors
  Bird strikes,…
Notes: ASN Aviation Safety Network
6

## Slide 7: RIMAS: RISK MANAGEMENT IN AVIATION SAFETY - A Framework and Architecture -
A comprehensive coherent methodology for aviation safety risk management at state level
Beyond risk matrices towards coherent development of SSPs
Key issues/steps:
Meaningfully exploring aviation safety databases
Building forecasting models for: operations, occurrences, severities
Assessing multiple consequences: deaths, injuries, delays, cancellations, maintenance and repair operations, image loss,…
Building risk maps (and matrices): Safety Risk Picture
Optimal assessment of aviation safety resources
Notes:   RIMAS is a new methodology with full use of numerous Operations Research methods, including Decision Analysis, Risk Analysis, Simulation, Bayesian Statistics, and Optimization, and implemented in a tool (in R! Language) that has allowed AESA to better support its safety decision making and attained savings in a number of areas.

## Slide 8: RESOURCE ALLOCATION
Influence Diagram

## Slide 9
INCIDENT RATES. FEATURES FACED IN (POISSON) RATES

## Slide 10
PREDICTING THE NUMBER OF OCCURRENCES
ID DLM+POISSON+(EXP)DLM
Model
Notes: We use a model in which both the number of operations and the occur-
rence rate evolve dynamically, as in Figure 3. For such purpose, we combine
in a novel way several standard models. Specifically, we use a Dynamic Linear
Model (DLM), see [11], to predict the number of operations (upper block); a
230 Poisson model to predict the number of occurrences given the rate and number
of operations (midblock); and, finally, a DLM to predict the evolution of the
occurrence rate (lower block). With this class of models, we are able to deal
with the effects we have found in the evolution of rates for all occurrence types,
mainly the possible presence of seasonal and trend components.

## Slide 11
PREDICTING OCCURRENCE CLASSES
We must also predict the corresponding occurrence classes (severities)
Model
assuming that the data Dt available until the beginning of the t-th period are ((s11, s21, ..., s51),. . .,(s1t−1, s2t−1,...,s5t−1)), and where sij represents the number of occurrences of class i, i ϵ {1, 2, 3, 4, 5}, in period j, j ϵ {1, . . . , t−1}:
Notes: We use a model in which both the number of operations and the occur-
rence rate evolve dynamically, as in Figure 3. For such purpose, we combine
in a novel way several standard models. Specifically, we use a Dynamic Linear
Model (DLM), see [11], to predict the number of operations (upper block); a
230 Poisson model to predict the number of occurrences given the rate and number
of operations (midblock); and, finally, a DLM to predict the evolution of the
occurrence rate (lower block). With this class of models, we are able to deal
with the effects we have found in the evolution of rates for all occurrence types,
mainly the possible presence of seasonal and trend components.

## Slide 12
PREDICTING INCIDENT CONSEQUENCES
  Multiattribute utility function
Notes: Forecasting deaths for 88 types of events and 4 types of aircrafts
Forecasting mild and severe injuries for 88 types of events and 4 types of aircrafts
…
Forecasting accidents for 88 types of events
Total of 1760 forecasting models (just for consequences)
Multiattribute utility function to evaluate them
Prediction of consequences and Loss function. We also must evaluate the consequences of various types and classes of incidents. We introduced a multiattribute utility function over eight identified consequences (see Section 2.2) and assessed it for all cases, together with a methodology to update it as consequence data accumulated

## Slide 13
RISK MAPPING
  Mapping (forecasted) incident numbers vs (forecasted) incident costs (expected, boxplots)
Less but more expensive | More and more expensive
Less and less expensive | More but less expensive
Notes: Safety mapping and occurrence screening. Based on our forecasting and consequence models, RIMAS uses simulation techniques to provide safety maps for all aviation occurrence types as well as a methodology for occurrence screening. A first use of RIMAS models allows for the screening of occurrences on which to focus the greatest efforts in safety risk management. To avoid some of the problems associated with risk matrices, RIMAS uses risk maps in which the (continuous) X axis refers to the likelihood of aviation occurrences and the (continuous) Y axis conveys consequences associated with such occurrences. L. Cox, What’s wrong with risk matrices?
However, as risk matrices are somewhat of a standard in aviation safety, we developed a method to transform a risk map into a risk matrix for communication purposes with other aviation agencies.
We later adjust the levels so that they are equidistant, according to the definition of risk matrices, achieved through simple affine transformations.

## Slide 14
USES: SCREENING

## Slide 15
SAFETY RESOURCE ALLOCATION
  RIMAS presents two versions of the general model:
    a) stochastic (using Monte Carlo simulation techniques)
    b) deterministic (based on the expected values of the relevant random variables)
  To be implemented depending on the level of accuracy required and the available computational resources

## Slide 16: RIMAS: THE ARCHITECTURE
Based on R! and ECCAIRS (and other aviation safety databases), it supports building:
Forecasting models for numbers of 90 types of occurrences (including number of operations)
Forecasting models for occurrence severity classes (1 to 5)
Forecasting models for occurrence consequences (deaths, delays,…)
A multiattribute utility function to assess such consequences
Risk maps (and risk matrices)
Screening of occurrences
Optimal assignment of resources to reduce and mitigate aviation safety risks
Displaying all types of graphs to build aviation safety reports

## Slide 17: RIMAS: THE ARCHITECTURE
DATA LOAD
Operations
Occurrences
RESOURCE ALLOCATION
FORECASTING
OPERATIONS
OCCURRENCES
OCCURRENCES SCREENING
RISK MAP
CORRELATION ANALYSIS
CONSEQUENCE ASSESSMENT
EFFECTS ANALYSIS
LINEAR
STRESS
GROUP
SEASONAL
RISK MATRIX
EXPLORATORY ANALYSIS
SEVERITY CLASSES
OCCURRENCES
GEO MAPS
RATES
INTERFACE

## Slide 18: EXPLORATORY ANALYSIS

## Slide 19: EFFECT ANALYSIS: GROUP

## Slide 20: EFFECT ANALYSIS: SEASONAL

## Slide 21: GEO MAPS

## Slide 22: CORRELATIONS MATRIX

## Slide 23: OPERATIONS FORECASTING

## Slide 24: RISK MAPS

## Slide 25
DISCUSSION
  Safety risk management is pervaded by simplistic methods based on risk matrices
  RIMAS provides a framework for safety risk management decisions in aviation safety at State level based on Data Science and engineering in action
  2 versions of the general model: stochastic and deterministic; depending on the level of accuracy required and the available computational resources
  RIMAS helps a National Aviation Safety Agency in identifying the best portfolio that may implement to improve aviation safety
  Trying to export to other countries for their national agencies and aviation industry + other business? (electrical networks, supply chain,…)
  Integrating Safety and Security
  Big Data! Data4Safety (EASA) + SafeClouds (H2020)